## Slide 1
Learning the Dynamics of an Under-actuated Adaptive Hand
Avishai Sintov, Andrew S. Morgan, Aaron M. Dollar, Kostas E. Bekris and Abdeslam Boularias

## Slide 2
Underactuated adaptive hands with compliant fingers are appealing due to their ability to passively adapt to objects of uncertain size and shape.
Therefore, they can provide a stable and robust grasp without tactile sensing or prior planning, and with open-loop control.
Adaptive hands

## Slide 3
Good models for adaptive hands are usually unavailable as they are hard and even impossible to derive.
Their intrinsic non-linearities along with many uncertainties such as joint and links flexibilities, friction and contacts are hard to model.
Adaptive hands

## Slide 4
Precise Manipulation Primitives proposed by Calli and Dollar approximates the kinematics of the hand and enables closed-loop visual servoing manipulations.
However, when applying these primitives, the object tends to move in non-linear arc-like trajectories.
Therefore, tracking a path can be challanging and motion planning cannot be applied.
Adaptive hands

## Slide 5
Our paper deals with learning of the dynamics model of an adaptive hand that would enable accurate predictions for motion planning, closed-loop control and policy-search algorithms.
Dynamics model

## Slide 6
In our work we focus on three questions:
When using local regression with Gaussian Process, how to choose the right nearest neighbors in the proximity of the query state-action pair?
What are the dominate features (e.g., object and links positions, actuators angles and torques) of an adaptive hand that are sufficient in describing its state and can provide accurate predictions?
Can a trained model based on these features and on transition data of a set of objects can generalize to provide accurate predictions for the manipulation of an unknown object?
Dynamics model

## Slide 7
We propose the Manifold Learning based Gaussian Process (MLGP) to select nearest neighbors based on the actual distance along the manifold, i.e., geodesic distance.
By utilizing diffusion maps, a known manifold learning technique, we can uncover the lower-dimensional subspace in which the data lies.
We choose the nearest neighbors for regression only in the lower dimensional space.
MLGP provides significant improvement compared to simple Euclidiean-based Gaussian Process (EGP).
Manifold learning

## Slide 8
Results
EGP compared to MLGP for three trajectories and a 20 mm cylinder

## Slide 9
In our we we focus on three questions:
What are the dominate features (e.g., object and links positions, actuators angles and torques) of an adaptive hand that are sufficient in describing its state and can provide accurate predictions?
Can a trained model based on these features and on transition data of a set of objects can generalize to provide accurate predictions for the manipulation of an unknown object?
When using local regression with Gaussian Process, how to choose the right nearest neighbors in the proximity of the query state-action pair?
Dynamics model

## Slide 10
We compare 7 feature configurations to represent the state space:
Object position.
Object position and distal links position.
Object position and all links positions.
Object position and actuators angles.
Object position and actuators loads.
Object position and, actuators angles and loads.
All measured features.
Feature configurations

## Slide 11
We compare 7 feature configurations to represent the state space:
Object position.
Object position and distal links position.
Object position and all links positions.
Object position and actuators angles.
Object position and actuators loads.
Object position and, actuators angles and loads.
All measured features.
Feature configurations
Results show that the objects position along with the actuators state (feature conf. 6) sufficiently embed the state of the system.

## Slide 12
We compare the use of a learned model to the model-free visual servoing proposed by Calli and Dollar.
Closed loop control